R1	Relay NC c5vdc→220vac (+manual)
R2	Relay NC c5vdc→220vac (+manual)
R3	Relay NC c220vav->220vac
C1	Contactor 2P NO 16A 220vac
C2	Contactor 2P NO 12A 220vac
C3	Contactor 2P NO 9A 220vac
PWM	Variable current source
UPS	12A input, 10A output
Panel parter
L1	L2	L3	N	G	grid
16A	fuse
L1	L2	L3	N	G	meter
NC	R1
16A	dif
L1	N	parter (high)
L1	N	C1
L1	L2	L3	N	G	bucatarie
16A	dif
Panel beci
L2	L3	G	3 phase beci
L1	N
NC	R2
L1	N	etaj
L123	N	C4
PWM
L1	N	pod
L1	N	C2
L1	N	microgrid
L1	N	microgrid
L1	N	lights parter
L1	N	extra load
L1	N	ups
L1	N	parter(low)
10A	fuse
L1	N	critical loads
Panel pod
Rack
CPU
10A	dif
L1	N	microgrid
NC	R3
ECU
L1	N	C3
L1	N	critical loads
L1	N	solar
L2
L2N
L2L3G
L2N
N
L1

---
Loads

---
Grid
Panels
L1 N
Large loads
L3
breaker relay
Critical loads
L3
Small loads
UPS
opener relay
extra load
breaker relay

---
3.6m
3.7m